## Slide 1
Up-to-date Post-Processors - What’s new in SC2021 SP4 -
Daniel Đurica
SolidCAM International Support manager

## Slide 2
Mill-Turn: Complete output control over interpolated 4th axis
arc_approximate and interpolation_for_distance in @start_of_job

## Slide 3
VMID: Support of Indexed Tool Stations
SC<=2020
SC2021
Real number of physical stations
Smaller .xml mach sim data
Easier Tool management

## Slide 4
“measure_orientation” in @def_turn, @def_turn_tool, @change_tool, @change_turn_tool, @start_of_job
Mill-Turn/Swiss-Type: Support of Indexed Tool Stations

## Slide 5
ToolKit: Sub-Tool support (Multi-Cutter Tool Item)
Property of each Turret. Default: No
Allows using different Tool Number per cutter within one tool assembly
Allows using different Tool ID per cutter
Resets Tool offset index per cutter

## Slide 6
Multi-Cutter Tool Item = NO
OR
01 – Station Number
11 – Offset Number
01 – Station Number
01 – Offset Number

## Slide 7
Multi-Cutter Tool Item = NO
OR
01 – Station Number (tool_position_in_turret)
11 – Offset Number
(tool_position*)
(d_offset – T)
(tool_offset_number – M)
OR
*Offset Number = tool_position_in_turret + (tool_position * 10 – 10)

## Slide 8
Multi-Cutter Tool Item = NO
OR
01 – Station Number (tool_position_in_turret)
11 – Offset Number
(tool_position*)
(d_offset – T)
(tool_offset_number – M)
OR
*Offset Number = tool_position_in_turret + (tool_position * 10 – 10)

## Slide 9
Multi-Cutter Tool Item = NO
OR
01 – Station Number (tool_position_in_turret)
11 – Offset Number
(tool_position*)
(d_offset – T)
(tool_offset_number – M)
OR
*Offset Number = tool_position_in_turret + (tool_position * 10 – 10)

## Slide 10
Multi-Cutter Tool Item = YES (Revolver)
Allows different Tool Number
Allows different Tool ID
Resets Tool offset index per cutter

## Slide 11
Multi-Cutter Tool Item = YES (Revolver)
Cutter_1/2 – Tool ID (tool_id_string)
D – Offset Number
(tool_position)
(d_offset – T)
(tool_offset_number – M)

## Slide 12
Multi-Cutter Tool Item = YES (Spindle)
Cutter_1/2 – Tool ID (tool_id_string)
D – Offset Number
(tool_position)
(d_offset – T)
(tool_offset_number – M)

## Slide 13
Multi-Cutter Tool Item = YES (Spindle)
Tool Number – 11
Tool ID – EINSTECHER D-Offset – D1/D2

## Slide 14
Multi-Cutter Tool Item = YES (Spindle)
Tool Number – 11
Tool ID – EINSTECHER D-Offset – D1/D2

## Slide 15
Multi-Cutter Tool Item = YES (Spindle)
Tool Number – 11
Tool ID – EINSTECHER D-Offset – D1/D2

## Slide 16
Conversion of Cutter cutting points from earlier versions

## Slide 17
Machine Simulation: New .xml stucture
Case study: Citizen M32-4M8

## Slide 18
Machine Simulation: New .xml stucture
Case study: Citizen M32-4M8
Reduced and simplified transformations
Eliminate limits with the number of used cutters in tool assembly
Added target_stock3/4/x in the case of multi-channel machines
<SC2021 SP4
SC2021 SP4
Simplifies the collision definition and performance
Reduce the loading time of machine simulation
220KB
18KB

## Slide 19
<SC2021 SP4
SC2021 SP4
Machine Simulation: New .xml stucture