## Slide 1: GPP&VMID - Tips and tricks
SolidCAM 2020
Danijel Đurica
SolidCAM International Support Manager

## Slide 2: Writing standardization of GPP and VMID
SolidCAM 2020

## Slide 3: Why we need convention
Convention of GPP writing

## Slide 4: Why we need convention
Convention of GPP writing
In SolidCAM GPPL none of the convention was declared so far
Allowing sharing Post-Processors within developers
When working in teams, it is very important to keep the coding style consistent and allow others easy debugging of your code and wise-versa.
Easier and effective debugging of other codes

## Slide 5: Add prefix to variable types
Naming the user-defined variables
n – numeric
b – logical
i – integer
s – string
n_Xpos n_XposSave n_FirstAxisAngle | b_FirstRapid b_StartOfJob b_ChangeTool | i_IndexJob i_ChannelID | s_JobName s_DrillCycleName
After prefix, insert the underscore. After underscore, start naming the variable with capital letter.

## Slide 6: Add prefix to variable types
Naming the user-defined variables
n – numeric
b – logical
i – integer
s – string
apos_f xlpos_f feed_f | xopos_f xcenter_rel_f bpos_f | spin_f xlnext_f radius_f | first_axis_angle_f second_axis_angle_f third_plane_angle_f
Note: Definition of the strings for formatting system variables should be defined without prefix.

## Slide 7: Add additional „L“ to local variable types
Naming the local variables
nL – numeric
bL – logical
iL – integer
sL – string
nL_Xpos nL_XposSave nL_FirstAxisAngle | bL_FirstRapid bL_StartOfJob bL_ChangeTool | iL_IndexJob iL_ChannelID | sL_JobName sL_DrillCycleName
Prefix for local user-defined variables have capital "L" letter next to prefix for variable type.
@usr_RotateToPlane (numeric nL_FirstAxisAngle numeric nL_SecondAxisAngle)

## Slide 8: Add additional „A“ to arrays
Naming the user-defined arrays
nA – numeric
bA – logical
iA – integer
sA – string
nLA_Xpos<<2>> | nA_XposSave<<2>> | bA_FirstRapid<<2>> | bLA_StartOfJob<<2>>
Prefix for user-defined arrays have capital “A" letter next to prefix for variable type.
nLA – numeric
bLA – logical
iLA – integer
sLA – string

## Slide 9: Add prefix “@usr_” to procedures
Naming user-defined @procedure/routine
Prefix for procedure/routine starts with "@usr_"
@usr_RapidMove
@usr_RotatePlane(numeric nL_FirstAngle, numeric nL_SecondAngle)

## Slide 10: Add prefix “MCO_” to MCO cycles/variables
Naming the MCO cycles/parameters/variables
nMCO – numeric
bMCO – logical
iMCO – integer
sMCO – string
Prefix for user-defined MCO variables should have capital "MCO" letters next to prefix for variable type followed with the underscore.
nMCO_Z1_PrePositioning nMCO_Spin bMCO_Synchronisation bMCO_UsePressure

## Slide 11: Add prefix “VMID_” to VMID variables
Naming the VMID parameters
nVMID – numeric
bVMID – logical
iVMID – integer
sVMID – string

## Slide 12: Add prefix “VMID_” to VMID variables
Naming the VMID parameters
In VMID we can declare the following parameters:
Machine options -------------------- (e.g. sVMID_MO_DrawingNum)
Milling Drill parameters --------- (e.g. nVMID_DM_DwellTime)
Turning Drill parameters ----------- (e.g. nVMID_DT_PeckDepth)
Probe parameters ------------------- (e.g. nVMID_P_ApproachZ)
Misc. Milling parameters ---------- (e.g. nVMID_M_HSCMode)
Misc. Turning parameters --------- (e.g. nVMID_T_ExactStop) (e.g. nVMID_TT_NumOfPasses)
(e.g. iVMID_TG_CustomCycle)

## Slide 13: Where new format should be used
General rules
Existing post-processor should be edited using used format
Use new format to new post-processors
Convert templates to new format

## Slide 14: Avoid calling the procedures more than 3 Levels!
General GPP rules
Debugging other codes are more difficult with post-processor whose structure have a call funtions on more than 3 Levels! Calling more than 3 Levels should be avoided if possible.

## Slide 15: Use Tabs and Spaces
General GPP rules
Use Tabs of indentation of your code
To improve reading of the code use Enter to split the sections of your code:
At beginning of procedure
Before and after main if/while statement

## Slide 16
General GPP rules

## Slide 17: Write GPP on English
General GPP rules
GUI – use local language
GPP – use English language

## Slide 18: Declare the variables in a row with explanation
General GPP rules

## Slide 19: Default for Milling VMID
Default MCO cycles based on machine kinematic

## Slide 20
Default Mill-Turn MCO cycles based on its kinematic
MCO cycles
Catch Part on MS and Synch On
Turret 1 – Retract X(Y) to reference
Turret 1 – Retract X(Y), Z to reference (left/right limit)
Turret 1 – Tool Change (with XY,Z,B retract)
Turret 1 – Tool Change and Z-preposition (with XY,Z,B retract)
Retracts
Tool Change
Part Transfer
Turret 1 – Retract XY, Z, B to reference
Catch Part on BS and Synch On
Pull Part in MS (BS)
Retract Back Spindle with Part
Retract Back Spindle without Part
Part Release
Turret n – Retract X(Y) to reference
Turret n – Retract X(Y), Z to reference (left/right limit)
Turret n – Retract XY, Z, B to reference
Turret n – Tool Change (with XY,Z,B retract)
Turret n – Tool Change and Z-preposition (with XY,Z,B retract)

## Slide 21: Implementation of C-axis interpolation cycle
SolidCAM 2020

## Slide 22
Everything you should know about it
G12.1/G112/TRANSPIT/…
Operator friendly for manual GCode programming/adjustments
Arc interpolation G02/G03 can be used
Radius Compensation can be used
XZY programming instead of XZC
Shorter Gcode in comparing to XZC
Better surface quality
For large parts with limited Y-axis stroke or narrow linear turret stations

## Slide 23
Example of manual programming
O0001; G54; T1010; M45; G28 H0; G97 S100 M13; G00 Z30.0; X80.0 Y0 C0; G98 G01 Z-20.0 F100; G18; G12.1(G112); .......... (4)
G42 X50.0; .............. (5) C25.0; ..................... (6) X-50.0;..................... (7) C-25.0; ................... (8) X50.0; .................... (9) C0; ......................... (10) G40 X100.0; ............ (11) G13.1(G113); …

## Slide 24
Programming habits
Programming drawing
O0001;
…
M45 (C-AXIS ON)
G28 H0 (C-AXIS REFERENCE)
G0 C0
G00 X31.4038 Y0. Z10. (Pre-position with OPOS set)
G01 F5000 (General feed for rapid move)
G05.1 Q1
G12.1 (START POLAR INTERPOLATION)
G01 X19. Z10. C-12.502 (Linear interpolation with HPOS set)
G01 Z2.
G01 Z-5. F300
G41 G01 C-9.5 F800
G01 X10.
G03 X-10. C-9.5 R-5. (Arc interpolation with HPOS set)
G01 X-19.
G01 C-2.
G03 X-15.9886 C7.7679 R5.
G03 X-19. C8. R5.
G01 C9.5
G01 X19.
G01 C5.
G03 X19. C-5. R-5.
G01 C-9.5
G40 G01 X25.004
G01 Z10. F5000
G13.1 (END POLAR INTERPOLATION)
G05.1 Q0
…

## Slide 25
Programming habits
Programming results on the machine
O0001;
…
M45 (C-AXIS ON)
G28 H0 (C-AXIS REFERENCE)
G0 C0
G00 X31.4038 Y0. Z10. (@start_of_job)
G01 F5000
G05.1 Q1
G12.1 (START POLAR INTERPOLATION)
G01 X19. Z10. C-12.502 (@move_5x)
G01 Z2.
G01 Z-5. F300
G41 G01 C-9.5 F800 (@line_5x)
G01 X10.
G03 X-10. C-9.5 R-5. (@arc_5x)
G01 X-19.
G01 C-2.
G03 X-15.9886 C7.7679 R5.
G03 X-19. C8. R5.
G01 C9.5
G01 X19.
G01 C5.
G03 X19. C-5. R-5.
G01 C-9.5
G40 G01 X25.004
G01 Z10. F5000
G13.1 (END POLAR INTERPOLATION) (@end_of_job)
G05.1 Q0
…
Prepositioning take unnecessary movements
Rapids are overwritten with G1 F5000
Successively jobs will reset C-axis to 0. each time
4th Axis Transform will reset C-axis to 0. after each transform

## Slide 26
Programming habits
Programming drawing and the results on the machine
O0001;
…
M45 (C-AXIS ON)
G28 H0 (C-AXIS REFERENCE)
G00 X31.4038 Y0. Z10. C-52.7696
G00 Z2.
G54
G05.1 Q1
G12.1 (START POLAR INTERPOLATION) (@move_5x)
G01 X31.4038 Z-5. C0. F300 (@line_5x)
G41 G01 X26.6234 C1.8163 F800
G01 X21.1782 C-1.7667
G03 X9.0778 C-9.7288 R-5.
G01 X3.6326 C-13.3117
G01 X-8.3106 C-8.774
G03 X-22.0432 C-1.6654 R5.
G03 X-24.2348 C-2.7238 R5.
G01 X-26.6234 C-1.8163
G01 X-3.6326 C13.3117
G01 X3.5333 C10.5891
G03 X19.4575 C4.5389 R-5.
G01 X26.6234 C1.8163
G40 G01 X30.2559 C4.2065
G13.1 (END POLAR INTERPOLATION) (@move_5x)
G00 Z10.
G05.1 Q0
…

## Slide 27: Implementation of coolant options
SolidCAM 2020

## Slide 28
Coolant code
@usr_coolingOnOFF(integer iL_OnOFF)
;iL_OnOff: 0=Explicit OFF | 1=Definition from CAM-Part
local integer iL_CoolantCorrFactor iL_MaxNoOfCooolantMCodes iL_MCodeCounter
iL_MaxNoOfCooolantMCodes = 4 ;MAX Number of M-Codes for Coolant in one Sentance
if (iL_OnOff eq 1 and flood_coolant eq 1 and !bA_CoolantActive<<i_TurretID,1>>) or (iL_OnOff eq 0 and bA_CoolantActive<<i_TurretID,1>>)
iL_MCodeCounter = iL_MCodeCounter + 1
if iL_MCodeCounter > iL_MaxNoOfCooolantMCodes or iL_OnOff eq 0
{nb,''}
endif
if flood_coolant > 0
iL_CoolantCorrFactor = -1
endif
{(9 - iL_OnOff+iL_CoolantCorrFactor):mcode_f} ;High Pressure=M07/M09 | Low Pressure M08/M09
bA_CoolantActive<<i_TurretID,1>>=iL_OnOff
endif
endp