## Slide 1
Up-to-date
Post-Processors - Part 7
Daniel Đurica
SolidCAM International Support manager

## Slide 2
Sub-Tool: Fully integrated in SP5
SC2021 SP4
SC2021 SP5

## Slide 3
New variable: Added stock_in in @setup

## Slide 4
Angular Holders: Guidelines for Post-Processor implementation

## Slide 5
Angular Holders: Guidelines for Post-Processor implementation
Fanuc - G68.1
Siemens – TRANS + ROT
Okuma – G127
Changes in GPP and VMID
is required
Does the machine controller have
a tilting cycle?
Changes in GPP
is required

## Slide 6
Angular Holders: On machines without tilting cycle
Machining possible on main planes (XY, YZ, ZX)
Arcs
Compensation
Drilling cycles
In non-parallel planes machining
Arcs must be interpolated!
Compensation can’t be used!
Drilling cycles are not possible!

## Slide 7
Angular Holders: On machines without tilting cycle
In non-parallel planes machining
Arcs are interpolated automatically by SolidCAM
Compensation output generates “Error” in trace (-9999)
Drilling cycles must be set to “No Cycle”
Machine plane generates “no_plane” in trace

## Slide 8
Angular Holders: On machines without tilting cycle
Changes in GPP – Implement rules
if omachine_plane eq no_plane
print 'Error plane!'
abort
endif
if side_o eq -9999
print 'Using compensation is not possible!'
endif
if omachine_plane ne xy or omachine_plane ne yz
print 'Drilling cycle can not be executed!'
endif

## Slide 9
Angular Holders: On machines without tilting cycle
For “dog leg” machine settings, the rapid movements should be avoided and converted into a cutting feed rate motion!
Changes in GPP – Implement rules
!

## Slide 10
Angular Holders: On machines with tilting cycle
Changes in VMID
Add Submachine with Custom Plane rotation (around X or Y)

## Slide 11
Angular Holders: On machines with tilting cycle
Changes in GPP
Implement local coordinate set output to:
@line
@rapid_move
@arc
@machine_plane
@compensation
@drill
@drill_point
Implement plane rotation cycle (G68.1, G127, ROT+TRANS,..etc)